Influence of structures on the stability constants values for some dyes formation formed by reactions of imines and the diazotized sulphanilic sodium salt

A.S.P.Azzouz                         M.M.H.Al-Niemi

College of Education , Mosul University

(NJC)

(Recevied on  2/12/2010) 		  (Accepted for publication  2/5/2011)

Abstract

The aims of this investigation were the determination of stability constants of some dyes formed by reactions of imines with diazotized sulphanilic sodium salt at different pH values and temperatures . These stability constants were evaluated spectrophotometrically by reactions of donor imines in a forms of oxime or Schiff bases with sulphanilic sodium salt as an acceptor . This study led to a comparison between stability constants values of similar imines in a forms of syn or anti oximes or Schiff bases having substituents as OH , NH2 , NO2 and CH3 groups on aromatic ring of primary amine parts of Schiff bases . Finally , results collected were interpreted and discussed in detail .

الخلاصة

يشتمل البحث على تعيين ثوابت استقرار الاصباغ المتكونة من تفاعلات الايمينات مع ملح الصوديوم لحامض السلفانليك المؤزوت في دوال حامضية ودرجات حرارية مختلفة . تضمن البحث استعمال الطريقة الطيفية في حساب ثوابت استقرار الاصباغ المتكونة من تفاعل الايمينات الواهبة للالكترونات والتي هي على اشكال اوكزيمات او قواعد شيف مع ملح الصوديوم لحامض السلفانليك المؤزوت المستقبل للالكترونات .

اهتمت الدراسة بمقارنة قيم ثوابت الاستقرار للايمينات المتشابهة والتي هي على شكل اوكزيمات سين وأنتي او قواعد شيف الحاوية على معوضات OH  , NH2 , CH3 على الحلقات الاروماتية المكونة للامين الاولي في قواعد شيف .

Introduction

During the last 28 years , a considerable interest had paid by the Chemist to the spectroscopical studies of imines by UV[1-3]  , IR[4-5] , NMR[6] and mass[7] spectra beside other kinetic[8], thermodynamic[9], tautomerism[9] and dyes[10] studies .

The diazotization reaction as analytical method was used for the determination of compounds such as 4-aminoantipyrine[11] , sulphonamide[12] , aniline[13], napthylamine[14] and nitrazipam[15] .

In our laboratory , Azzouz     etal[16-18]  had studied the stability constants of some azo dyes formation between donor imines with sulphanilic sodium salt as an acceptor . These consecutive reactions included the determination of structures[16] of imines by physical method the stoichiometry[17] and the stability constants18 of the dyes mentioned . These publications led the authors to study of influence of pH with the type of oxime isomer[17] and surfactant[18] on the stability of the dyes . Experimentally , all these physical parameters mentioned were found to be effective in determining the values of stability constants .

This work describes the influence of different structures of imines on the stability constants values of a dyes . These imines are derived from the mother compound  2,4-dihydroxy benzaldehyde and are in a forms of syn or anti oxime or Schiff bases having substituents as OH-  , NH2 and CH3 on the aromatic rings of primary amine parts .

Experimental

All chemicals used throughout this work were supplied by Fluka origin. The  synthesis of imines in a forms of Schiff bases or syn and anti oximes12 are followed , by using a similar procedures. Products are obtained by reactions of 2,4 dihydroxy- benzaldehyde with an appropriate primary amines , purified by recrystallization in ethanol , dried and collected. The chemical structures of these imines are identified and confirmed by using physical method such as m.p,s , UV and IR spectra as cited in our previous communication[16].

Preparation of solutions

- 2×10-3M reagent of diazonium salt as derived from sulphanilic sodium salt was prepared by a standard method[17]. Then after it was diluted to 10-3M by distilled water.

- 0.1M Na2CO3 and 2N HCl as basic and acidic solutions respectively , were prepared by a standard method. These solutions were used to obtain the pH values of 5.4 , 7.1 and 9.2 during dye stability constant study. Na2CO3 is elected among other bases , due to its capability to give a maximum absorbance value of yellow dye.

Instrumentation

- A computerized double beam uv_visible Shimadzu , 1601 spectro-photometer, matched silica cell of dimensions 1×1×3cm3 are used. All absorbance measurements were performed versus blank.

- Single beam Cecil CE 1011/1000 spectrophotometer.

- pH measurements were achieved by using pw 9400 pH meter (Philips).

- Water bath L200 (Memmert) was used to regulate the temperature of dye solutions , whenever is required in a range between 20-60Cº.

Results and Discussion

The stability constant value K of the dye product DA is formed by the reaction of donor-acceptor mechanism[16] is evaluated from the following reaction:-

D + A                 DA     ,  where    D and A are imine donor and the diazonium salt molecule acceptor respectively. DA is the dye product.

The value of stability constant K is evaluated[17] experimentally from equation (1)  of the form :  K =   ……(1)

C= molar concentration of the dye

α = degree of dissociation of the dye as defined in equation (2)

α=      …… (2)

Es = Absorbance of the dye at 1:1 stoichiometric ratio

Em = Absorbance of the dye at optimal conditions

The stability constants of a dyes formation between donor imines and sulphanilic sodium salt were studied spectrophotometrically . Their stability constant values were determined at fixed pH and temperature as shown in Table (2) . The pH were selected at values 5.4 , 7.2 and 9.2 . Similarly , the temperature were varied in a range (283-323)K . In order interpret the stability constant values clearly the following division of results were thought necessary :-

- Comparison of stability constant of aldehyde DHBAL with syn DHBO

and anti DHBD .

At pH values 5.4 and 7.4 , the following arrangement was observed

Ksyn DHBO > KAnti DHBO > K DHBAL

At  pH  value  9.2  ,  it  was  impossible to determine the stability constant

values  at  all  five  temperature as in  Table (1)  ,  due  to  the    tautomerism reaction3  DHBAL  and  anti DHBO  show some stability  constant  values  and some temperatures which were difficulty compared .

- Comparison of DHBAL with unsubstituted Schiff bases DHBA .

At  pH 7.1  ,  Table (2)  shows  a higher  stability  constant  values  for unsubstituted  Schiff  bases  DHBA  when  compared   with  DHBAL  with exclusion  of  temperature  283K . This  was due  to  the presence  of  two and one  aromatic  ring  in  DHBA  and  DHBAL respectively . Therefore , the  donation19  property  of  DHBA  was  greater  than  DHBAL  and consequently accompanied by greater stability constants in DHBA according to donor acceptor mechanism of complex formation .

- Comparison of DHBA with other Schiff bases .

This paragraph was divided in to Schiff bases that contain substituents OH ,  NH2 , NO2 and CH3 at different positions on aromatic ring of primary amine part . Hence the following division are required :-

(a) Schiff bases that contain OH group on the amine part .

Form literature , it was known that OH group had values of σm = 0.121 , σp = -0.37  . This means that such group had acceptor and donor properties at meta and para positions respectively . The behavior of OH  at ortho position had nearly a similar electronic effect to para . This was in addition to the steric effect and intramolecular hydrogen bond formation of OH at ortho position .

It was observed that stability constants values of DHBA as in Table (2) at pH values 5.4 , 7.1 and all temperatures  had a greater values when compared with similar Schiff bases having OH group in ortho , meta and para position . The cause for the lower stability constant values of Schiff bases having OH group in meta position was due to the capability of such group to behave as an acceptor as seen above from σm value mentioned . Originally it was anticipated that Schiff bases DHB-p-hydroxyaniline having a higher stability constant value , due to the negative value of σp stated before . This was experimentally accompanied by increasing the electronic density around to donor site in Schiff base .

Actually , the reverse of such result was expected experimentally in these Schiff bases due to possibility of hydrogen bond formation in OH group and the planarity of Schiff bases . The planarity was studied20 by comparing the molar extension coefficient Σmax of Schiff bases containing OH group in ortho , meta and p-positions . Estimated Σmax  had a values of 2040 , 1770 and 450 in unit of L.mol-1.cm-1 in Schiff bases DHB-o-HA , DHB-m-HA and DHB-p-HA respectively . The first and second numbers had approximate values and near similar planarity . The low Σmax value for DHB-p-HA means that such molecule is less planar and accompanied by low value of stability constant . Schiff bases DHB-m-HA did not show any stability constant value at pH 5.4 and all temperatures , due to complete protonation3 of nitrogen atom at such acidic medium . At pH 9.2  , the stability constants values for Schiff bases contain OH group show a variable results . It was believed that these hydroxylic Schiff bases undergo the enol         keto tautomerism reaction before dye formation . The last is fully accepted to Schiff bases DHB-p-HA at temperature range (303-323) K as in Table (2) .

(b) Schiff bases that contain NH2 group

Table (2) showed unstable dye formation at pH 5.4 and temperature 283k for Schiff bases DHBA , DHB-o-HA and DHB-p-AA. The complete protonation of Schiff bases was a good answered to such case .

In the meantime , these Schiff bases showed a stable dyes at temperature 293K with the following arrangement of stability constant as :

KDHBA > KDHB-OAA > KDHB-P-AA

Also these amino Schiff  bases showed a variable stability constant values at pH 7.1 and 0.2 which were difficulty compared .

(c) Schiff bases that contain CH3 group

These Schiff bases showed a stable dyes at some temperatures and pH values . The stability constants values collected were increased in the following arrangement :-

KDHB-m-MA > KDHB-p-MA > KDHB-o-MA

Methyl group as known[19] as a good donor when present at para and meta positions on the aromatic rings . At ortho position, such group exerts some steric effect. The last effect was responsible on increasing stability constant values of the dye . Maximum stability constant value of the dye DHBA was observed when compared with others substituted methyle DHBA at some temperatures and pH 5.4 and 7.1 with exclusion the temperature 323K at pH 7.1 . The planarity statement stated before might be effective in this case . ∑max estimated for ortho and para methylated DHBA had values of 1112 , 361 in unit Liter.mole-1.cm-1 respectively . The greater ∑max value of ortho substituent resulted to greater stability constant value . A reverse to such result was true at pH 9.2 . This means that DHBA had a lower stability constant values than the methylated DHBA at some temperatures . In otherwords , a lower probability for tautomerism process  was occurred in methylated DHBA , resulted to increase stability constants value or the dye .

(d) Schiff bases that contain NO2 group

In this study all ortho , meta and para substituted nitro DHBA showed unstable dyes formation . This was due to the strong electronic acceptor property of nitro group . The last was cleared from σp and σm values of +0.778 and +0.710 respectively .

The nitro group in substituted DHBA resulted to an electron deficiency around the donor site in nitro Schiff bases . Certainly , this attributed by decreasing the probability of dye formation .

This supported the dye formation by donor – acceptor mechanism21 .

The failure determination of stability constants for substituted nitro DHBA dyes were in full agreement with DHB-m-HA at all temperatures and pH 5.4 . The σm for OH group had value +0.121 , which means that such group was electron acceptor .

The influence of OH , NH2 and CH3 substituents in DHBA on the stability constants of dyes formation was accomplished by the use of Hammett equation19  at temperature 20Cْ  , using the following equation :-

Log K / K0 = σp                ….… (1)

K = stability constant for substituted dye .

K0 = stability constant for unsubstituted dye .

P = reaction constant (sensitivity)

σ = Sigma constant .

From equation(1) the plot of log K / K0 versus σ showed a linear lines with negative slope . Typical plots were shown in Fig. 1 for the meta and para substituted DHBA and at different pH values . The negative values of slopes in Fig.1 , mean that dye formation was accelerated by donor electron groups in substituted DHBA . This was in full agreement[21] with dye or complex formation . Carful examination of linear plot in Fig. 1 showed an intercept for each line . This was in disagreement with theoretical study of linear plot . The answered to such abnormal result was due to the high stability of dyes formed by reaction of DHB-p-AA with diazotized sulphanilic sodium salt at different pH values . Actually DHB-p-AA contained an amino group , and by help of resonance , the negative charge spread over eight resonance forms as in Scheme (1) . This enhanced the negative charge and consequently the donor site in DHB-p-AA and resulted to a greater stability constant values of dye mentioned .

Conclusions

- A spectrophotometric method was used in the determination of dyes formations by reactions of imines derived from the mother compound 2 , 4-dihydroxybenzaldehyde .

- Imines under study were prepared by standard method and their chemical structures were confirmed[16] by the physical means , namely , UV , IR and melting points .

- The stability constants for dye formation between imines under study and diazotized sulphanilic sodium salt were governed by the following   factors :-

- The chemical structure of imine

- The temperature

- The pH of the medium

- Steric effect if available in imine

- Planirity of imine

Tabel  (1) : Symbol , nomenclature and some physical constants of Imines.

| Comp. No. | Symbol of 2,4- Comp. Derivatives | Nomenclature | Colour | m.p. (oC) | Structure |
| --- | --- | --- | --- | --- | --- |
| 1 | DHBAL | 2,4-dihydroxy benzaldehyde | pink | 134-136 |  |
| 2 | Syn DHBO | Syn-2,4-dihydroxy benzaldoxime | milky | 188-190 |  |
| 3 | Anti DHBO | Anti-2,4-dihydroxy benzaldoxime | colourless | 110-112 |  |
| 4 | DHBA | 2,4-dihydroxy benzylidene aniline | deep red | - |  |
| 5 | DHB-o-HA | 2,4-dihydroxy benzylidene-o-hydroxy aniline | red | - |  |
| 6 | DHB-m-HA | 2,4-dihydroxy benzylidene-m-hydroxy aniline | mild red | - |  |
| 7 | DHB-p-HA | 2,4-dihydroxy benzylidene-p-hydroxy aniline | red | - |  |
| 8 | DHB-o-AA | 2,4-dihydroxy benzylidene-o-amino aniline | sandy | - |  |
| 9 | DHB-p-AA | 2,4-dihydroxy benzylidene-p-amino aniline | red | - |  |
| 10 | DHB-o-MA | 2,4-dihydroxy benzylidene-o-methyl aniline | red | - |  |
| 11 | DHB-m-MA | 2,4-dihydroxy benzylidene-m-methyl aniline | mild red | - |  |
| 12 | DHB-p-MA | 2,4-dihydroxy benzylidene-p-methyl aniline | red | - |  |
| 13 | DHB-o-NA | 2,4-dihydroxy benzylidene-o-nitro aniline | orange | - |  |
| 14 | DHB-m-NA | 2,4-dihydroxy benzylidene-m-nitro aniline | yellow | - |  |
| 15 | DHB-p-NA | 2,4-dihydroxy benzylidene-p-nitro aniline | yellow | - |  |

Table (2) : Stability constant values for the dyes at different pH and temperatures

| Comp. No. | Symbol of 2,4- Comp. Derivatives | pH | T (K) |  |  |  | K (l. mol-1) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | DHBAL | 5.4 | 283 | 0.157 | 0.031 | - | - |
|  |  |  | 293 | 0.155 | 0.043 | - | - |
|  |  |  | 303 | 0.018 | 0.122 | 0.85246 | 10151.6 |
|  |  |  | 313 | 0.015 | 0.121 | 0.87603 | 8076.7 |
|  |  |  | 323 | 0.012 | 0.116 | 0.89655 | 6434.9 |
|  |  | 7.1 | 283 | 0.155 | 0.163 | 0.04908 | 19738281.3 |
|  |  |  | 293 | 0.157 | 0.177 | 0.11299 | 3473625.0 |
|  |  |  | 303 | 0.019 | 0.025 | 0.24000 | 659722.2 |
|  |  |  | 313 | 0.039 | 0.005 | - | - |
|  |  |  | 323 | 0.009 | 0.037 | 0.75676 | 21237.3 |
|  |  | 9.2 | 283 | 0.161 | 0.079 | - | - |
|  |  |  | 293 | 0.153 | 0.045 | - | - |
|  |  |  | 303 | 0.005 | 0.007 | 0.28571 | 437500.0 |
|  |  |  | 313 | 0.006 | 0.011 | 0.45455 | 132000.0 |
|  |  |  | 323 | 0.004 | 0.014 | 0.71429 | 28000.0 |
| 2 | Syn DHBO | 5.4 | 283 | 0.230 | 0.244 | 0.05738 | 14316326.5 |
|  |  |  | 293 | 0.240 | 0.264 | 0.09091 | 5500000.0 |
|  |  |  | 303 | 0.234 | 0.273 | 0.14286 | 2100000.0 |
|  |  |  | 313 | 0.228 | 0.299 | 0.23746 | 676175.4 |
|  |  |  | 323 | 0.221 | 0.310 | 0.28710 | 432458.0 |
|  |  |  | 333 | 0.813 | 0.645 | - | - |
|  |  | 7.1 | 283 | 0.607 | 0.634 | 0.04259 | 26394924.6 |
|  |  |  | 293 | 0.577 | 0.620 | 0.06936 | 9673877.8 |
|  |  |  | 303 | 0.687 | 0.981 | 0.29969 | 398853.2 |
|  |  |  | 313 | 0.686 | 0.603 | - | - |
|  |  |  | 323 | 0.672 | 0.593 | - | - |
|  |  |  | 333 | 0.617 | 0.503 | - | - |
|  |  | 9.2 | 283 | 0.644 | 0.594 | - | - |
|  |  |  | 293 | 0698 | 0.625 | - | - |
|  |  |  | 303 | 0.715 | 0.485 | - | - |
|  |  |  | 313 | 0.680 | 0.486 | - | - |
|  |  |  | 323 | 0.687 | 0.581 | - | - |
|  |  |  | 333 | 0.672 | 0.593 | - | - |
| 3 | Anti DHBO | 5.4 | 283 | 0.013 | 0.015 | 0.13333 | 2437500.0 |
|  |  |  | 293 | 0.011 | 0.015 | 0.26667 | 515625.0 |
|  |  |  | 303 | 0.012 | 0.023 | 0.47826 | 114049.6 |
|  |  |  | 313 | 0.011 | 0.037 | 0.70270 | 30103.6 |
|  |  |  | 323 | 0.011 | 0.009 | - | - |
|  |  | 7.1 | 283 | 0.020 | 0.023 | 0.13043 | 2555555.6 |
|  |  |  | 293 | 0.023 | 0.029 | 0.20690 | 926388.9 |
|  |  |  | 303 | 0.025 | 0.039 | 0.35897 | 248724.5 |
|  |  |  | 313 | 0.028 | 0.054 | 0.48148 | 111834.3 |
|  |  |  | 323 | 0.013 | 0.005 | - | - |
|  |  | 9.2 | 283 | 0.054 | 0.070 | 0.22857 | 738281.3 |
|  |  |  | 293 | 0.055 | 0.075 | 0.26667 | 515625.0 |
|  |  |  | 303 | 0.060 | 0.045 | - | - |
|  |  |  | 313 | 0.058 | 0.033 | - | - |
|  |  |  | 323 | 0.026 | 0.021 | - | - |
| 4 | DHBA | 5.4 | 283 | 0.044 | 0.042 | - | - |
|  |  |  | 293 | 0.036 | 0.039 | 0.07692 | 7800000.0 |
|  |  |  | 303 | 0.043 | 0.038 | - | - |
|  |  |  | 313 | 0.036 | 0.032 | - | - |
|  |  |  | 323 | 0.041 | 0.039 | - | - |
|  |  | 7.1 | 283 | 0.054 | 0.041 | - | - |
|  |  |  | 293 | 0.032 | 0.033 | 0.03030 | 52800000.0 |
|  |  |  | 303 | 0.054 | 0.058 | 0.06897 | 9787500.0 |
|  |  |  | 313 | 0.053 | 0.063 | 0.15873 | 1669500.0 |
|  |  |  | 323 | 0.039 | 0.058 | 0.32759 | 313296.4 |
|  |  | 9.2 | 283 | 0.054 | 0.069 | 0.21739 | 828000.0 |
|  |  |  | 293 | 0.049 | 0.077 | 0.36364 | 240625.0 |
|  |  |  | 303 | 0.028 | 0.063 | 0.55556 | 72000.0 |
|  |  |  | 313 | 0.023 | 0.099 | 0.76768 | 19710.9 |
|  |  |  | 323 | 0.011 | 0.119 | 0.90756 | 5611.3 |
| 5 | DHB – o – HA | 5.4 | 283 | 0.137 | 0.211 | 0.35071 | 263942.7 |
|  |  |  | 293 | 0.088 | 0.147 | 0.40136 | 185808.7 |
|  |  |  | 303 | 0.086 | 0.154 | 0.44156 | 143209.3 |
|  |  |  | 313 | 0.091 | 0.185 | 0.50811 | 95263.7 |
|  |  |  | 323 | 0.085 | 0.178 | 0.52247 | 87466.8 |
|  |  | 7.1 | 283 | 0.216 | 0.241 | 0.10373 | 4164480.0 |
|  |  |  | 293 | 0.209 | 0.245 | 0.14694 | 1975501.5 |
|  |  |  | 303 | 0.220 | 0.270 | 0.18519 | 1188000.0 |
|  |  |  | 313 | 0.157 | 0.204 | 0.23039 | 724943.4 |
|  |  |  | 323 | 0.225 | 0.326 | 0.30982 | 35923.6 |
|  |  | 9.2 | 283 | 0.148 | 0.191 | 0.22513 | 76413.2 |
|  |  |  | 293 | 0.145 | 0.205 | 0.29268 | 412847.2 |
|  |  |  | 303 | 0.149 | 0.222 | 0.32883 | 310358.4 |
|  |  |  | 313 | 0.136 | 0.223 | 0.39014 | 200343.5 |
|  |  |  | 323 | 0.130 | 0.229 | 0.43231 | 151872.3 |
| 6 | DHB – m – HA | 5.4 | 283 | 0.185 | 0.145 | - | - |
|  |  |  | 293 | 0.176 | 0.159 | - | - |
|  |  |  | 303 | 0.101 | 0.055 | - | - |
|  |  |  | 313 | 0.112 | 0.064 | - | - |
|  |  |  | 323 | 0.123 | 0.093 | - | - |
|  |  | 7.1 | 283 | 0.126 | 0.156 | 0.19231 | 1092000.0 |
|  |  |  | 293 | 0.130 | 0.164 | 0.20732 | 922145..3 |
|  |  |  | 303 | 0.132 | 0.177 | 0.25424 | 576888.9 |
|  |  |  | 313 | 0.121 | 0.177 | 0.31638 | 341470.0 |
|  |  |  | 323 | 0.118 | 0.173 | 0.31792 | 337421.5 |
|  |  | 9.2 | 283 | 0.062 | 0.064 | 0.03125 | 49600000.0 |
|  |  |  | 293 | 0.062 | 0.065 | 0.04615 | 22388888.9 |
|  |  |  | 303 | 0.057 | 0.062 | 0.08065 | 7068000.0 |
|  |  |  | 313 | 0.058 | 0.068 | 0.14706 | 1972000.0 |
|  |  |  | 323 | 0.056 | 0.077 | 0.27273 | 488888.9 |
| 7 | DHB – p – HA | 5.4 | 283 | 0.022 | 0.027 | 0.18519 | 1188000.0 |
|  |  |  | 293 | 0.025 | 0.033 | 0.24242 | 644531.3 |
|  |  |  | 303 | 0.033 | 0.032 | - | - |
|  |  |  | 313 | 0.040 | 0.018 | - | - |
|  |  |  | 323 | 0.044 | 0.015 | - | - |
|  |  | 7.1 | 283 | 0.064 | 0.066 | 0.03030 | 52800000.0 |
|  |  |  | 293 | 0.055 | 0.059 | 0.06780 | 10140625.0 |
|  |  |  | 303 | 0.050 | 0.057 | 0.12281 | 2908163.3 |
|  |  |  | 313 | 0.052 | 0.042 | - | - |
|  |  |  | 323 | 0.053 | 0.045 | - | - |
|  |  | 9.2 | 283 | 0.055 | 0.063 | 0.12698 | 2707031.3 |
|  |  |  | 293 | 0.047 | 0.058 | 0.18966 | 1126446.3 |
|  |  |  | 303 | 0.048 | 0.044 | - | - |
|  |  |  | 313 | 0.052 | 0.037 | - | - |
|  |  |  | 323 | 0.059 | 0.031 | - | - |
| 8 | DHB – o – AA | 5.4 | 283 | 0.030 | 0.029 | - | - |
|  |  |  | 293 | 0.019 | 0.021 | 0.09524 | 4987500.0 |
|  |  |  | 303 | 0.027 | 0.030 | 0.10000 | 4500000.0 |
|  |  |  | 313 | - | 0.017 | - | - |
|  |  |  | 323 | 0.022 | 0.018 | - | - |
|  |  | 7.1 | 283 | 0.028 | 0.033 | 0.15152 | 1848000.0 |
|  |  |  | 293 | 0.033 | 0.041 | 0.19512 | 1057031.3 |
|  |  |  | 303 | 0.024 | 0.032 | 0.25000 | 600000.0 |
|  |  |  | 313 | 0.023 | 0.033 | 0.30303 | 379500.0 |
|  |  |  | 323 | 0.028 | 0.042 | 0.33333 | 300000.0 |
|  |  | 9.2 | 283 | 0.032 | 0.007 | - | - |
|  |  |  | 293 | 0.041 | 0.043 | 0.04651 | 22037500.0 |
|  |  |  | 303 | 0.026 | 0.030 | 0.13333 | 2437500.0 |
|  |  |  | 313 | 0.022 | 0.034 | 0.35294 | 259722.2 |
|  |  |  | 323 | 0.015 | 0.037 | 0.59460 | 57334.7 |
| 9 | DHB – p – AA | 5.4 | 283 | 0.052 | 0.041 | - | - |
|  |  |  | 293 | 0.029 | 0.048 | 0.39583 | 192797.8 |
|  |  |  | 303 | 0.050 | 0.017 | - | - |
|  |  |  | 313 | 0.045 | 0.028 | - | - |
|  |  |  | 323 | 0.054 | 0.005 | - | - |
|  |  | 7.1 | 283 | 0.057 | 0.058 | 0.01724 | 165300000.0 |
|  |  |  | 293 | 0.061 | 0.065 | 0.06154 | 12390625.0 |
|  |  |  | 303 | 0.048 | 0.060 | 0.20000 | 1000000.0 |
|  |  |  | 313 | 0.031 | 0.064 | 0.51563 | 91092.8 |
|  |  |  | 323 | 0.052 | 0.043 | - | - |
|  |  | 9.2 | 283 | 0.044 | 0.019 | - | - |
|  |  |  | 293 | 0.063 | 0.077 | 0.18182 | 1237500.0 |
|  |  |  | 303 | 0.063 | 0.081 | 0.22222 | 787500.0 |
|  |  |  | 313 | 0.053 | 0.071 | 0.25352 | 580709.9 |
|  |  |  | 323 | 0.035 | 0.033 | - | - |
| 10 | DHB – o – MA | 5.4 | 283 | 0.070 | 0.079 | 0.11392 | 3413580.3 |
|  |  |  | 293 | 0.072 | 0.084 | 0.14286 | 2100000.0 |
|  |  |  | 303 | 0.071 | 0.086 | 0.17442 | 1356888.9 |
|  |  |  | 313 | 0.073 | 0.093 | 0.21505 | 848625.0 |
|  |  |  | 323 | 0.075 | 0.101 | 0.25743 | 560281.1 |
|  |  | 7.1 | 283 | 0.076 | 0.085 | 0.10588 | 3987654.3 |
|  |  |  | 293 | 0.076 | 0.088 | 0.13636 | 2322222.2 |
|  |  |  | 303 | 0.104 | 0.127 | 0.18110 | 1248393.2 |
|  |  |  | 313 | 0.078 | 0.101 | 0.22772 | 744612.5 |
|  |  |  | 323 | 0.079 | 0.110 | 0.28182 | 452133.2 |
|  |  | 9.2 | 283 | 0.078 | 0.088 | 0.11364 | 3432000.0 |
|  |  |  | 293 | 0.077 | 0.3089 | 0.13483 | 2379513.9 |
|  |  |  | 303 | 0.070 | 0.083 | 0.15663 | 1718934.9 |
|  |  |  | 313 | 0.073 | 0.090 | 0.18889 | 1136678.2 |
|  |  |  | 323 | 0.081 | 0.104 | 0.22115 | 796219.3 |
| 11 | DHB – m - MA | 5.4 | 283 | 0.004 | 0.013 | 0.69231 | 32098.8 |
|  |  |  | 293 | 0.004 | 0.016 | 0.75000 | 22222.2 |
|  |  |  | 303 | 0.012 | 0.011 | - | - |
|  |  |  | 313 | 0.009 | 0.003 | - | - |
|  |  |  | 323 | 0.017 | 0.010 | - | - |
|  |  | 7.1 | 283 | 0.002 | 0.003 | 0.33333 | 300000.0 |
|  |  |  | 293 | 0.001 | 0.007 | 0.85714 | 9722.2 |
|  |  |  | 303 | 0.002 | 0.001 | - | - |
|  |  |  | 313 | 0.003 | 0.001 | - | - |
|  |  |  | 323 | 0.005 | - | - | - |
|  |  | 9.2 | 283 | 0.002 | 0.001 | - | - |
|  |  |  | 293 | 0.002 | 0.004 | 0.50000 | 100000.0 |
|  |  |  | 303 | 0.001 | 0.006 | 0.83333 | 12000.0 |
|  |  |  | 313 | 0.004 | 0.002 | - | - |
|  |  |  | 323 | 0.003 | - | - | - |
| 12 | DHB – p - MA | 5.4 | 283 | 0.117 | 0.193 | 0.39378 | 195472.7 |
|  |  |  | 293 | 0.096 | 0.173 | 0.44509 | 140057.4 |
|  |  |  | 303 | 0.099 | 0.197 | 0.49746 | 101535.8 |
|  |  |  | 313 | 0.083 | 0.186 | 0.55376 | 72759.0 |
|  |  |  | 323 | 0.080 | 0.205 | 0.60976 | 52480.0 |
|  |  | 7.1 | 283 | 0.116 | 0.216 | 0.46296 | 125280.0 |
|  |  |  | 293 | 0.110 | 0.218 | 0.49541 | 102794.9 |
|  |  |  | 303 | 0.122 | 0.257 | 0.52529 | 86019.2 |
|  |  |  | 313 | 0.096 | 0.218 | 0.55963 | 70303.7 |
|  |  |  | 323 | 0.092 | 0.226 | 0.59292 | 57897.1 |
|  |  | 9.2 | 283 | 0.074 | 0.085 | 0.12941 | 2599173.6 |
|  |  |  | 293 | 0.097 | 0.120 | 0.19167 | 1100189.0 |
|  |  |  | 303 | 0.088 | 0.122 | 0.27869 | 464359.9 |
|  |  |  | 313 | 0.085 | 0.072 | - | - |
|  |  |  | 323 | 0.090 | 0.044 | - | - |

Scheme (1) :The influence of resonance in DHB-p-AA

Fig. 1 : Relationship between log K / K0 versus σ for dyes formed by reactions of m and p – substituted DHBA with donor .

References

  - A.S.P.Azzouz and A.B.N.Al-Dabagh, Nat.J.Chem. 2008, 32, 677 .

- A.A.Saeed , A.W.Sultan , S.A.Selman and N.A.Abood , Can.J.Spectros. , 1983 , 28 , 104 .

- A.S.P.Azzouz and A.N.Obed Agha , Physical Chem. An Indian J. , 2007 , 2(3) , 15 .

- A.S.P.Azzouz , A.A.Rahman and A.G.Taki , J.Edu.Sci. , 2003 ,15(2) , 1 .

- A.A.Saeed , N.A.Abood , N.A.Al-Mosoudi and G.T.Matti , Can.J.Spectros. , 1985 , 30, 142 .

- Ed.S.Patai , "The Chemistry of Carbon Nitrogen Double Bond" , John Wiley , New York , 149-180 .

- A.S.P.Azzouz , Spectros. Letter , 1995 , 28 , 1 .

- A.S.P.Azzouz , K.A.Abdullah and Kh.I.Al-Niemi , Microchem. J , 1991 , 43 , 54 .

- A.S.P.Azzouz , Z. Phys.Chem. , 2002 , 216 , 1 .

- A.S.P.Azzouz and A.N.Obed Agha , Nat.J.Chem. , 2008 , 30 , 251 .

- M.Q.Al-Abachi, A.M.S.Al-Delamie and S.Al-Najafi , Analyst , 1985 , 113 , 1661.

- P.Nagaraja , R.Kallonchiva , A.Ramanathapure and S.H.Yathirajan, J.Pharmaceutics and Biopharmaceutics , 2002 , 53 , 187 .

- J.S.E.Romero , E.F.S.Alfonso , M.C.G.Alvarez- Coque and G.R.Ramos , Analyt. Chim. Acta , 1990 , 235 , 317 .

- T.I.Younis and W.A.Bashir , Talanta , 1995 , 42 , 1121 .

- T.S.Al-Ghabsha , A.S.P.Azzouz and A.N.O. Agha , J.Edu.Sci. , 2008 , 21(1) , 147.

- A.S.P.Azzouz and M.M.Al-Niemi , J.Edu.Sci. , 2009 , 21(1) , 1 .

- A.S.P.Azzouz and M.M.Al-Niemi , Tikrit J.Pure Sci. , 2008 , 13(3) , 118 .

- A.S.P.Azzouz and A.N.Obed Agha , J.Edu.Sci. 2005 , 17 , 10 .

- A.Streitwieser and J r C.H.Heathcock , " Introduction to Organic Chemistry " , 1981 , 2nd ed. New York .

- J.R.Majer and A.S.P.Azzouz , J.Chem.Soc.Farad. Trans. 1 , 1983 , 79 , 675 .

- A.Martin , " Physical pharmacy " , 1993 , 4th ed. Laa and Febiger , Philadelphia , London , pp. 251-370 .

# Text boxes

2

O

N

H

O

O

H

N

H

C

2

O

N

H

O

O

H

N

H

C

N

2

O

H

O

O

H

N

H

C

3

H

C

H

O

O

H

N

H

C

3

H

C

H

O

O

H

N

H

C

C

3

H

H

O

O

H

N

H

C

2

H

N

H

O

O

H

N

H

C

N

2

H

H

O

O

H

N

H

C

H

O

H

O

O

H

N

H

C

H

O

H

O

O

H

N

H

C

O

H

H

O

O

H

N

H

C

H

O

O

H

N

H

C

O

H

N

H

O

O

H

H

C

H

O

N

H

O

O

H

H

C

H

O

O

H

O

H

C

p-OH

p-NH2

m-CH3

p-CH3

p-NH2

p-OH

m-CH3

p-NH2

p-CH3

m-CH3